## Slide 1
Budgets, Reserves
And
Financially Sustainable Communities
September 9, 2025
Peter B. Miller, RS, EBP
Presented by:

## Slide 2: Topics:
Module 1: Importance of Reserves
Module 2: Basic Tenets
Module 3: Financially Sustainable Communities
Module 4: Sample Reserve Study
Module 5: The Board’s Involvement
Module 6: Cash Flow vs. Component
Module 7: Inflation CPI v. PPI

## Slide 3
The Importance of Reserves
Module 1

## Slide 4: What are Reserves?
Replacement Reserves? Money budgeted each year for the replacement and major repair of common elements.
Replacement Reserve Studies? Financial forecasting report used to assist Boards in establishing appropriate annual Reserve Funding Levels in Budget.

## Slide 5: Why are Reserves Important?
Adequate Reserves help to Protect, Preserve and Enhance the property values in your community.

## Slide 6
“Perhaps the greatest
Duty of the Board of
Directors is to Protect,
Preserve and Enhance
the value of the homes
within the community!”
Robert Lyles, Esq. Charleston, SC

## Slide 7: How Do Reserves protect property values?
Ensure that funding is available for timely replacement.
Stabilize Annual Assessment.
Spread replacement costs equitably over time.

## Slide 8: Is the Board Required to do a Reserve Study?
Not all States require Reserve Studies.
Governing Docs. may provide Board the authority to establish Reserves in budget.
Boards still have a Fiduciary Duty to make prudent, business-like decisions.
Maintaining Reserves is considered Industry “Best-Practice” and “Industry Standard”.

## Slide 9: Reserve Study Levels
Level I
  Full Study w/ Onsite Condition Assessment.
Level II
  Reserve Study Update w/ On-site Condition Assessment
Level III
  Reserve Study Update w/o On-site Condition
  Assessment
Level IV
  Preliminary Reserve Study (from Drawings)

## Slide 10: What are Reserve Components
Commonly-Owned Physical Asset (check governing documents)
Will require major repair or replacement
Suggested Resolution of the Board:
  Normal Economic Life > 3 Years
  Replacement Cost > $X,XXX

## Slide 11: National Reserve Study Standards as Revised 2023
Must update every three years.
Must include funding for major maintenance.
Must include funding for periodic Structural Evaluations. *
* For some types of buildings.

## Slide 12: Engaging a Qualified Reserve Study Provider
Designated Reserve Specialists (RS).
Flexible with revisions and Zoom mtgs.
DO NOT SELECT BASED UPON LOW BID! There is a difference between cost and value!
Board should read Sample Report!
Provides Cash Flow Method of Calculation*.
  *More realistic method of calculating Reserves.

## Slide 13: Why We Plan For Reserves
Legal
Practical/Financial
Ethical

## Slide 14: Legal Considerations
State Statutes
Governing Documents
IRS Guidelines
Bank Loan Requirements
Fiduciary Duty of Board
Freddie/Fannie Requirements

## Slide 15: Practical / Financial Considerations
PROTECT PROPERTY VALUES!
Sound Financial Planning!
10% - 50% of Annual Budget!
Avoid Special Assessments!
Equitable Distribution of costs over time!

## Slide 16: Ethical Considerations
Avoids “kicking the can down the road” (future financial obligations) to future or long-term owners!
Equitable Distribution of costs over time! “Everybody pays their fair share!” *
*Not an easy sell among some demographics!

## Slide 18
Three Basic Tenets of a
Reserve Study
Module 2

## Slide 19
Tenet #1:
The Reserve Study must be readable and understandable in order to be usable!

## Slide 20
Tenet #2:
The Reserve Study must reflect the priorities, the plans, the hopes, and the aspirations of the community!

## Slide 21
Tenet #3
The Reserve Study funding recommendation must be practical and implementable!

## Slide 22: Reasonable Expectations!
A Reserve Study is a visual condition assessment.
It is not an in-depth technical study or structural evaluation.
Increase the accuracy of the Study by bringing in your professional experts! i.e., HVAC, Bathymetry, Paving, etc.

## Slide 24
Financially Sustainable Communities
Module 3

## Slide 25: Where do the Reserves fit in the budgeting process?
Maintenance & Operations
Reserves

## Slide 26: Three distinct purposes
Operations
Maintenance
Reserves

## Slide 27: Operations Costs
Costs related to operating the “Corporation”
Utilities
Management Fees
Personnel
Taxes
Consultants
  Attorneys
  Accountants
  Architects
  Engineers
  Etc.

## Slide 28: Maintenance Costs
All costs associated with maintaining the “Brick and Mortar” aspects of the “Corporation”.

## Slide 29: Replacement Reserve Costs
Funds set aside as part of the annual budget for the major repair and replacement of the commonly-owned components of the community.

## Slide 30: Financially Sustainable Community!
Operations
Maintenance
Reserves

## Slide 32
Sample
Reserve Study
Module 4

## Slide 35
Starting Balance $77,240
Current Funding $90,000
Recommended Funding $150,000

## Slide 41
Projected Annual Expenditures are show by individual year in this bar graph.

## Slide 42
Cash Flow
$150,000
Current Funding
$90,000
Cumulative totals of Annual Expenditures shown in this graph. See page A1 and A4

## Slide 44
The Board’s Involvement
Module 5

## Slide 45: Board Involvement
Establish inventory.
Set threshold policy: (Board Resolution)
  Lasts longer than “X”
  Costs more than “Y”
Provide data, guidance, contractor names, and historical context.
Set Minimum Fund Balance.

## Slide 46: Board Involvement (continued)
Review draft:
  Provide priorities and other input.
  Replacement timing, replacement costs, etc.
Investigate alternatives.
Develop Strategic Funding Plan.

## Slide 47
6%

## Slide 48
100%
100%
100%

## Slide 50
Cash Flow
$150,000
Current Funding
$90,000

## Slide 51: What’s the Next Step?
You as the Manager…
You as a Board Member…
You as a Finance Committee Member…

## Slide 52: What’s the Next Step?
You just were handed this report!
It says to increase the Reserve Funding from $90K to $150K!
What?
That’s a $60K annual increase!
Holy Cr@p!

## Slide 53: What Are Your Alternatives?
Increase Normal Assessments
Special Assessment
Commercial Bank Loan
Combination of two or more

## Slide 54: Next Step:
Review inventory data.
Re-think replacement priorities.
Check Cash Flow margins.
Develop Strategic Funding Plan.

## Slide 55: Check Cash Flow Margins
Year end balance stays positive until year 2030.

## Slide 56
This association has the latitude to “ramp up” rather than have one large increase.

## Slide 57
Cash Flow - $150,000
Current Funding - $90,000

## Slide 58: Strategic Funding Plan
Ramp Up Annual Funding over five years:
Year 1: $90K to $102K
Year 2: $102K to $114K
Year 3: $114K to $126K
Year 4: $126K to $138K
Year 5: $138K to $150K *
*Year 5 would bring Reserve Study update and would adjust for inflation, underfunding, changed conditions.

## Slide 60
Cash Flow Method
Versus
Component Method
Module 6

## Slide 61: CASH FLOW VS COMPONENT (Pooling vs. Full Funding)
CASH FLOW (“Pooling”) METHOD
  Treats Reserves as an aggregate “pool” of funds to adequately fund each year.
COMPONENT (“Full Funding”) METHOD
  Treats each Reserve Item as a separate “line item” budget to adequately fund each item.

## Slide 62: Illustration of the Different Mathematical Models
One Project per year,
Projects repeat every 4 yrs
Cost of $12,000 per Project
Four Projects:
  Year One - Parging,
  Year Two - Seal Coat,
  Year Three - Plumbing,
  Year Four - Retaining Wall
(Assume $Zero Starting Balance) (Assume $Zero Threshold)

## Slide 63: Cash Flow Calculations
 | Year | 1st | 2nd | 3rd | 4th | Total
COMPONENT | Cost x $1,000 | Annual Contributions |  |  |  | 
Parging Year One | $12 | 3 | 3 | 3 | 3 | $12
Paving Year Two | $12 | 3 | 3 | 3 | 3 | $12
Plumbing Year Three | $12 | 3 | 3 | 3 | 3 | $12
Retaining Wall Year Four | $12 | 3 | 3 | 3 | 3 | $12
Total Cost | $48 | $12 | $12 | $12 | $12 | $48

## Slide 64: Component Calculations
 | Year | 1st | 2nd | 3rd | 4th | Total
COMPONENT | Cost x $1,000 | Annual Contributions |  |  |  | 
Parging Year One | $12 | 12 | 3 | 3 | 3 | $21
Paving Year Two | $12 | 6 | 6 | 3 | 3 | $18
Plumbing Year Three | $12 | 4 | 4 | 4 | 3 | $15
Retaining Wall Year Four | $12 | 3 | 3 | 3 | 3 | $12
Total Cost | $48 | $25 | $16 | $13 | $12 | $66

## Slide 65
Cash Flow Recommendation: $48K
Component Recommendation: $66K
Component Method requires 38% more funding than Cash Flow.
Cash Flow would be 72% of “Full Funding” if using Component Method.
Comparison:
Copyright @ Miller Dodson Associates 2022

## Slide 66: Actual Reserve Study
$56,026
$36,791
$27,768

## Slide 68
Inflation
and
Reserve Fund Planning
Module 7

## Slide 69: Understand Inflation - CPI vs PPI
Consumer Price Index (CPI)
  Food Costs
  Fuel Costs
  Electricity Costs
  Housing Costs (meaning rent)
Producer Price Index (PPI)
  Manufacturing costs
  Construction costs

## Slide 76: DIVE BRIEF:
Tariff fears tied to biggest construction cost jump in 2 years.
Contractors have rushed to buy materials before potential tariffs go into effect, pushing prices higher. More hikes could lie ahead, according to construction trade associations.
Construction DIVE
February 13, 2025

## Slide 77: Dive Brief:
Construction input prices jumped 1.4% in January, marking the largest monthly increase in two years, according to an analysis by Associated Builders and Contractors.
Energy costs drove much of that increase, with crude petroleum, natural gas and unprocessed energy all rising.
However, the price jump also stems from a rush to purchase materials ahead of potential tariffs, said Anirban Basu, ABC chief economist. The cost of inputs to construction now sits 40.5% higher than February 2020, according to the report.

## Slide 79: Take Aways
Reserves are necessary to establish a Financially Sustainable Community!
Reserves help protect property values!
Board (and Manager) has an active role in producing an accurate Reserve Study!
Use the Cash Flow Method of calculation!
Inflation is an important consideration in Reserve Planning.

## Slide 80: PDF of this presentation is available at
MillerDodson.com

## Slide 81
Questions

## Slide 82: Speaker Profile
Peter B. Miller, RS, EBP, has worked professionally with community associations, both as an Architect and a Reserve Specialist, for over 35 years. He is one of the most widely recognized authorities in the field of Replacement Reserves and Reserve Fund Planning. A frequent author and speaker, his article “The Reserve Truth – What We Must Learn from the Surfside Florida Tragedy” was published in CAI’s internationally distributed Common Ground magazine.
Peter served on the Community Associations Institute’s (CAI) National Reserve Study Standards Committee that developed the CAI National Reserve Study Standards in the 1990’s and was appointed by CAI’s President a Co-Chair for the “Reserve, Maintenance, and Building Safety Task Force”. Peter served on CAI's National Board of Trustees from 2018 through 2022. Peter has also served as a “Subject Matter Expert” on Reserve Study legislation for the Commonwealth of Virginia, as well as the States of Maryland and Delaware.
The Firm of Miller Dodson Associates specializes in Reserve Studies and conducts between 850 – 1,000 Reserve Studies annually.
Peter and his wife, Kathy, split their time between their award-winning historic home in Annapolis, Maryland and their home in Cape Charles on the lower Eastern Shore of Virginia.

## Slide 84
Thank You!